## Slide 1
Mitigation Planning Workshop Module 2: Risk Assessment
Notes: Students will be able to:
Understand risk assessment terminology
Recognize hazards and community needs
Determine potential losses to vulnerable community assets
Be able to summarize their community’s vulnerability to the identified hazards

## Slide 2: Unit 1 Risk Assessment

## Slide 3: Risk Assessment
Process that collects information and assigns values to risks to:
    Identify or compare courses of action
    Develop priorities
    Inform decisionmaking
Foundation for mitigation strategy to reduce future losses
Notes: Also used for THIRAs, Emergency Response Plans, Recovery Plans

## Slide 4: Risk Assessment Terms
Natural Hazard
Community Asset
Vulnerability
Impact
Risk
Notes: Have students read each one!

## Slide 5: Venn Diagram
Note: Modified from U.S. Geological Survey and Oregon Partnership for Disaster Resilience Models.
NATURAL HAZARDS
Location
Extent
(Magnitude/Strength)
Previous Occurrences
Future Probability
COMMUNITY ASSETS
Population
Built Environment
Natural Environment
Economy
RISK

## Slide 6: Multi-Jurisdiction Considerations
Describe unique or varied hazards
Assess assets and risks for each jurisdiction
Town
County
District
Tribe
City
Multi- Jurisdiction

## Slide 7: Steps to Assess Risks
Describe Hazards
Identify Community Assets
Analyze Risks
Summarize Vulnerability

## Slide 8: Updating the Risk Assessment
Changes in hazards (example: disaster declarations, new data, new hazard occurrences)
Changes in community assets
    Emphasis on changes in development

## Slide 9: Unit 2 Describe Hazards

## Slide 10: Step 1: Describe Hazards
Describe Hazards
Identify Community Assets
Analyze Risks
Summarize Vulnerability

## Slide 11: Types of Hazards
Natural Hazard
Technological Hazard
Human-caused Hazard
Climate Change
Notes: Natural hazards must be addressed in a plan; however some communities may choose to assess other hazards in their planning process

## Slide 12: Hazard Mitigation & Climate Adaptation
“CLIMATE ADAPTATION is a process that intends to reduce long-term risks from hazards associated with climate variability and climate change.”
        Baltimore Disaster Preparedness Plan

## Slide 13: Hazard Mitigation & Climate Adaptation
SOURCE - Integrating Hazard Mitigation and Climate Adaptation Planning: Case Studies and Lessons Learned, ICLEI

## Slide 14: Relationship between Adaptation and Hazards Risk
SOURCE: OR Natural Hazard Mitigation Plan, Chapter 2. Risk Assessment
Notes: Illustrate how climate change may exacerbate already existing hazards. Discuss benefits of integrating climate adaptation in existing processes/assessments; as opposed to a separate climate action plan.

## Slide 15: Sources of Hazard Information
State Hazard Mitigation Plan
Disaster declarations
Hazard-related reports/plans
State and federal agencies
Colleges/universities
Planning team and stakeholders
Local knowledge and records

## Slide 16: Discussion Questions
What natural hazards affect your community?
What information sources would you use for your plan?

## Slide 17: Hazard Descriptions
Location
Extent
Previous Occurrences
Probability of Future Events

## Slide 18: Location

## Slide 19: Location
From 2010 Deschutes County Natural
Hazards Mitigation Plan

## Slide 20: Extent
Magnitude
Severity
Speed of Onset
Duration of event
Notes: Extent defines the characteristics of the hazards regardless of the people and built environment it affects
while
Impacts refers to the effect of a hazard on the people and property in the community

## Slide 21: Extent
Notes: This map shows potential depth of water during a flood in Moab, UT

## Slide 22: Extent
From 2010 Deschutes County Natural Hazards Mitigation Plan
Notes: This shows the Condition Class for the wildfire hazard;

## Slide 23: Changes to Hazards Location & Extent
Notes: This will impact current and future shoreline development. The impacts of rising sea level on communities will continue to present significant short- and long-term challenges.

## Slide 24: Changes to Hazards
    Wildfire:
“Climate change has the potential to affect multiple elements of the wildfire system: fire behavior, ignitions, fire management, and vegetation fuels. Hot dry spells create the highest fire risk. Increased temperatures may intensify wildfire danger by warming and drying out vegetation. Climate change also may increase winds that spread fires.”
        King County, WA HMP
Notes: Won’t read off the slide, but use it as an example of a plan addresses exacerbation to existing hazards.

## Slide 25: Previous Occurrences
Date of Flood | Property Damage
September 12, 2002 | $25,000
July 30, 1999 | $2,000
July 14, 1999 | $60,000
September 6, 1997 | $175,000
July 31, 1976 | $50,000
September 18, 1972 | $385
July 29, 1969 | $1,250
August 2, 1963 | $5,000
Date of Flood | Property Damage
August 19, 2010 | $2,500,000
August 28, 2007 | $1,000
July 23, 2007 | $1,000
October 14, 2006 | $15,000
October 9, 2006 | $20,000
October 6, 2006 | $500,000
October 3, 2006 | $25,000
July 10, 2006 | $25,000
September 9, 2005 | $3,000
Source of data: http://webra.cas.sc.edu/hvri/products/sheldus.aspx
Notes: When data are available, describe the extent of the event and the impacts that occurred, such as fatalities and injuries, building and infrastructure damage, and loss of services
Illustrates information on previous occurrences of flooding from the Colorado River in Grand County, UT

## Slide 26: Probability of Future Events
The previous slide shows:
    There were 17 occurrences of flooding in Grand County, UT
    Over 48 years from 1962 through 2010
With 17 occurrences in 48 years, probability of future occurrence is 17/48 = 0.3542 or about a 35% chance of flooding in any year
Notes: Probability: Likelihood of the hazard occurring in the future
Maybe defined using historical frequencies or statistical probabilities
If using terms such as “highly likely”, “likely”, “unlikely”, then they must be defined

## Slide 27: Changing Probabilities
“Idaho’s State Hazard Mitigation Plan (SHMP) is taking critical steps to decrease and potentially avoid these impacts associated with climate change….
Vulnerabilities include:
    Increased occurrences and magnitudes of hazard events, including: severe storms, flooding, drought, and wildland fires
    Changing climatic and precipitation patterns that may impact the State’s agricultural, hydroelectric, recreational, and economic sectors
    Increased exposure to hazard events for all of Idaho’s citizens and infrastructure
    Expanding diversity of extreme weather events
    Increased temperatures and altered streamflows impacting the ecosystem and species migration “
Notes: How much do you risk? Different risk thresholds for different assets; for wanting lowest risk, don’t just take historic trends into consideration.

## Slide 28: Hazard Map
Location
Extent
Previous occurrences
Reference: Toe River Region, NC Hazard Mitigation Plan
Notes: This map of the Toe River watershed in North Carolina shows the location of previous hail events, indicates the extent or size of the hail, and shows the number of previous occurrences

## Slide 29: Hazard Map
Location
Extent
Probability
USGS Washington 2014 Seismic Hazard Map 2% in 50 years Peak Ground Acceleration Hazard (%g)
http://earthquake.usgs.gov/hazards/
Notes: This map shows Peak Ground Acceleration (PGA) for Washington. It identifies the locations with the greatest EQ risk, the extent of the risk based on a scientific scale, and probability of damage based on location

## Slide 30: Summarize Hazard Information
Hazard | Location | Extent | Probability
Tornado | Entire planning area | EF2 | 2% chance per year
Hail | Entire planning area | 1” diameter | 10% chance per year
Flood | Along 0.2 mile of stream in Town A only | 6” to 12” depth | 25% chance per year

## Slide 31: Summarize Hazard Information
Hazard | Yes/No | Decision to Profile Hazard
Avalanche | No | Shaktoolik’s topography is not one likely to produce avalanches; no instances of avalanches havv been observed in Shaktoolik.
Earthquake | Yes | Designated as a hazard in Alaska All‐Hazard Risk Mitigation Plan. Community members remember feeling the 1964 Earthquake. However, no earthquakes have been felt since 1964.
Erosion | Yes | Designated as a hazard due to extensive history of erosion.
Example excerpt from City of Shaktoolik/Shaktoolik Tribal
Council, Alaska Multi‐Jurisdictional Hazard Mitigation Plan

## Slide 32: Questions?

## Slide 33: Unit 3 Identify Community Assets
Notes: Students will be able to identify the community assets that are vulnerable to identified hazards

## Slide 34: Step 2: Identify Community Assets
Describe Hazards
Identify Community Assets
Analyze Risks
Summarize Vulnerability

## Slide 35: Community Assets
People
Economy
Structures
Critical Facilities and Infrastructure
Natural Environment
Notes: Ask yourself, “What’s important to us?”

## Slide 36: Discussion Question
What are assets in your community?

## Slide 37: People
Locations and concentrations of residents and employees
Locations and concentrations of special needs and dependent populations
Types and locations of visiting populations

## Slide 38: Economy
Major employers
Primary economic sectors
Commercial centers
Dependencies between economy and infrastructure

## Slide 39: Structures
Existing and Future
Locations, types, and values of structures
Cultural and historic resources
Locations and types of planned new development/redevelopment
Infrastructure for new development
Planned critical facilities and capital improvements
Notes: QUESTION: Why identify future development?
QUESTION: How can we identify future development? Think about Buildable Lands Inventory

## Slide 40: Structures (Existing and Future)
Existing Structures
(red dots)
Existing (red dots) and Future Structures
(yellow dots)
Source: FEMA Region VIII, undated

## Slide 41: Critical Facilities and Infrastructure
Location, age, and value of critical facilities and infrastructure
Dependencies that exist among critical facilities and infrastructure

## Slide 42: Natural Environment
Environmental functions that reduce magnitude of hazards
Critical habitat areas to protect
Hunting, gathering, and/or fishing areas
Areas where conservation reduces risk and achieves other community objectives (example: trails and parks)
Other cultural and historic natural resources
Notes: This is key to reducing risk
Wetland Mitigation Banking
Prescribed Fire
Forest health/logging

## Slide 43: Unit 4 Analyze Risks and Summarize Vulnerability
Notes: Students will be able to:
Determine potential impacts to vulnerable community assets
Summarize community’s overall vulnerability to the identified hazards

## Slide 44: Step 3: Analyze Risks
Describe Hazards
Identify Community Assets
Analyze Risks
Summarize Vulnerability

## Slide 45: Natural Hazards, Community Assets, and Risk
Note: Modified from U.S. Geological Survey and Oregon Partnership for Disaster Resilience Models.
NATURAL HAZARDS
Location
Extent
(Magnitude/Strength)
Previous Occurrences
Future Probability
COMMUNITY ASSETS
Population
Built Environment
Natural Environment
Economy
RISK

## Slide 46: Assess Impacts and Vulnerability
For each hazard
Evaluate vulnerable assets
Assess potential impacts
Estimate future losses
Notes: Regardless of how the results are expressed or methods of analysis used, this step must result in….
a description of the potential impacts
of each hazard
for each participating jurisdiction in the plan

## Slide 47: Methods for Analyzing Risk
Exposure analysis
Historical analysis
Scenario analysis

## Slide 48: Exposure Analysis
What assets are located in hazard-prone areas?
Quantify number, type, value of assets
Estimate future development in hazard-prone areas based on planning and zoning
Consider magnitude of hazard or event (high vs. moderate wildfire hazard areas)
Use maps and GIS for analysis

## Slide 49: Exposure Analysis
Notes: This table summarizes exposure by providing the full value of structures in flood zones; it does not estimate potential loss; damage will not typically equal 100% of the value of a structure

## Slide 50: Historical Analysis
Based on past events, what are potential future impacts and losses?
Use for higher frequency events with available data on past impacts and losses (e.g., winter storms, stormwater flooding)
Consider vulnerability of new development

## Slide 51: Hazards Suitable for Historical Analysis
Drought
Flooding
Severe Winter Weather
Notes: Frequent events with lots of data to support

## Slide 52: Scenario Analysis
What are the potential impacts and losses if a particular event occurs?
Monetary costs, casualties, down time, etc.
Consider a scenario analysis for low-frequency, high-consequence events (e.g., earthquake)
Use modeling tools, such as Hazus
Notes: * Scenario analysis asks “what if” a particular event occurred
* Tool for assessing low-frequency, high-consequence events, such as earthquakes

## Slide 53
[INSERT Image]
100-yr
Notes: Slide shows the population along the Colorado River in Moab. The information can be used to estimate the number of displaced individuals and short-term shelter needs for a flood scenario

## Slide 54
100-yr
Building Type
Notes: This slide shows relative amount of estimated damages or economic losses due to flooding along Colorado River in Moab, UT.

## Slide 55: Risk Index
Hazard | Location | Probability | Extent | Impact | Rank
Tornado | Entire planning area | 5% chance per year | EF2 | Damage > $35 million | 1
Hail | Entire planning area | 75% chance per year | Up to 1” diameter | Damage $50,000 to $100,000 | 2
Subsidence | Northwest corner of planning area | Very low; there is no history of subsidence | Minimal | Damage <$500 | 3
Notes: Useful way to compare results

## Slide 56: Risk Index
Example excerpts from Washington State Hazard Mitigation Plan

## Slide 57: Step 4: Summarize Results
Describe Hazards
Identify Community Assets
Analyze Risks
Summarize Vulnerability

## Slide 58: Summarize Overall Vulnerability
Summarize each jurisdiction’s overall vulnerability to hazards
Communicate findings to:
    Educate public, stakeholders, elected officials
    Inform decisionmaking
    Develop mitigation strategy

## Slide 59: Develop Problem Statements
To communicate vulnerabilities, develop problem statements
Clear, concise
Not overly technical
Identify key issues or problems
Based on results of the risk assessment
Pertain to specific community assets or hazards
Pertain to individual jurisdictions or to the entire planning area
Notes: QUESTION: Who has actually done this?

## Slide 60: Example Problem Statements
Newberg City recently annexed the South Woods area located in the wildland-urban interface. The City’s land use and building codes do not address wildfire hazard areas. Future development in South Woods will increase vulnerability to wildfires.
The North Creek Sewage Treatment Plant is located in the 100-year floodplain and has been damaged in past events.

## Slide 61: Example Problem Statements
Residents of the Village describe ground failure impacts such as some homes and facilities sinking on their pilings, particularly in the downtown “old town” area.
The boardwalk to the new school, which is used for evacuation, has ground failure damage.
In addition, the community’s marine fuel header has begun to sink into the ground and slant to one side.
Example excerpts from Village of Kongiganak Draft Hazard Mitigation Plan

## Slide 62: Activity 2.1: Develop a Problem Statement for Your Community Allotted Time: 30 minutes
In your small group, discuss the hazards, assets, and risks that exist in your communities. Based on your small group discussion, choose two problems statements to share with the group as a report out. The problem statement should describe a specific risk to one of the communities in your group.

## Slide 63: Update to Reflect Development Changes
Increasing vulnerability
Climate change
New development in hazard-prone areas
Decreasing vulnerability
Mitigation actions implemented to reduce risk
Adopted codes to protect future development
Notes: Plan updates must describe changes in development that have occurred since the last plan was approved.

## Slide 64: Risk Assessment Summary
Plan document focuses on communicating analysis and findings to:
    Emergency managers
    Planners
    Policy makers
    Community members
Background data in appendices or integrated in local systems

## Slide 65: Review of the Risk Assessment
For each hazard, the plan must provide
Description of:
  Hazards (location, extent, previous occurrences, and future probability)
  Potential impacts for each participating jurisdiction
  Repetitively damaged NFIP-insured structures (More on this in Module 3)
  Changes in development since previous plan was developed if plan is an update
Summary of vulnerability

## Slide 66: Questions?